## Slide 1: Program: ESE 4009 INSTRUCTOR: Prof. Mike Aleshams
Group 6
Rohan Yadav C0773871 Shahrukh Padaniya C0769542 Swapnil Sevak C0777195 Vandana Ega C0777215
Presented by: SWAPNIL SEVAK

## Slide 2: Project : Iot based cradle using SIDS monitor

## Slide 3: Real time operation

## Slide 4: What is real time operation?
A real-time operation is an operation designed to support real-time applications that process data in real time, without buffer delays.
Processing time requirements are measured in tenths of seconds or smaller time increments (including any OS delay).
A time-bound system with well-defined, definite time restrictions is known as a real-time system.
The system will fail if processing is not done within the given limits. They are either time-sharing or event-driven.

## Slide 5: What is real time operation
Time-sharing systems move between tasks based on clock interruptions, whereas event-driven systems switch between jobs depending on their priorities.
A pre-emptive scheduling method is used by the majority of real time operation.

## Slide 6: Advantages of real time operation
Priority Based Scheduling.
Abstracting Timing Information.
Maintainability/Extensibility.
Modularity.
Promotes Team Development.
Easier Testing.
Code Reuse.
Improved Efficiency.

## Slide 7: Disadvantages of real time operation
Limited Tasks.
Use Heavy System resources.
Complex Algorithms.
Device driver and interrupt signals.
Thread Priority

## Slide 8: PTHREAD_SETSCHEDPARAM
SYNOPSIS
#include <pthread.h>
int pthread_setschedparam(pthread_t thread, int policy, const struct sched_param *param);
int pthread_getschedparam(pthread_t thread, int *restrict policy, struct sched_param *restrict param);

## Slide 9: Description
The pthread setschedparam() method configures the thread's scheduling strategy and parameters.
policy defines the thread's new scheduling policy.
The policy values that are supported.
The new schedule is specified by the structure pointed to by param.
Thread's parameters The criteria for scheduling are kept in the structure is as follows:
struct sched_param { int sched_priority; /* Scheduling priority */ };

## Slide 10: Description
The pthread getschedparam() method retrieves the thread's scheduling policy and parameters, which are stored in the policy and param buffers, respectively.
The priority value returned is the one set by the thread's most recent pthread setschedparam(), pthread setschedprio(3), or pthread create(3) function.
Calls to any priority inheritance or priority ceiling methods (for example, pthread mutexattr setprioceiling(3) and pthread mutexattr setprotocol(3)) will not affect the returned priority.

## Slide 11: Return Value
These routines return 0 on success and a nonzero error number on failure.
The scheduling policy and parameters of the thread are not altered if pthread setschedparam() fails.

## Slide 12: Possible Errors
The following mistake can occur in both of these functions:
ESRCH There was no thread with the ID thread.
The following problems can cause pthread setschedparam() to fail:
EINVAL policy isn't recognised, or param isn't relevant to the policy.
EPERM The caller lacks the necessary permissions to change the given scheduling policy and parameters.For pthread setschedparam,
POSIX.1 additionally lists an ENOTSUP ("effort was made to set the policy or scheduling parameters to an invalid value") issue ().

## Slide 13: Example
The programme below shows how to use pthread setschedparam() and pthread getschedparam(), as well as a number of other pthreads methods related to scheduling.
The main thread sets its scheduling policy to SCHED FIFO with a priority of 10, and creates a thread attributes object with a scheduling policy attribute of SCHED RR and a scheduling priority value of 20 in the subsequent run.
The programme then sets the inherit scheduler attribute of the thread attributes object to PTHREAD EXPLICIT SCHED (using pthread attr setinheritsched(3)), indicating that threads created with this attributes object should use the thread attributes object's scheduling attributes.

## Slide 14: Code for Pulse Oximeter
#include <stdio.h>
#include <stdlib.h>
#include <pthread.h>
#include<fcntl.h>
#include<unistd.h>
#include<termios.h> // using the termios.h library
#include<string>
#include<iostream>
#include <wiringPi.h>

## Slide 15: Code for Pulse Oximeter
#define NUM_THREADS 2
/* create thread argument struct for thr_func() */
typedef struct _thread_data_t {
int tid;
double stuff;
} thread_data_t;

## Slide 16: Code for Pulse Oximeter
/* thread function */
void *thr_func(void *arg) {
if(wiringPiSetup() == -1){
printf("setup wiringPi failed !");
exit(1);
}
pinMode( 29, OUTPUT );
digitalWrite( 29, HIGH );
sleep(1);
unsigned char hr[100];
int file, count;

## Slide 17: Code for Pulse Oximeter
if ((file = open("/dev/ttyAMA0", O_RDWR | O_NOCTTY | O_NDELAY))<0) {
perror("UART: Failed to open the file.\n");
pthread_exit(NULL);
}

## Slide 18: Code for Pulse Oximeter
struct termios options; // the termios structure is vital
tcgetattr(file, &options); // sets the parameters for the file
// Set up the communications options:
// 115200 baud, 8-bit, enable receiver, no modem control lines
options.c_cflag = B115200 | CS8 | CREAD | CLOCAL;
options.c_iflag = IGNPAR | ICRNL; // ignore parity errors
tcflush(file, TCIFLUSH); // discard file information
tcsetattr(file, TCSANOW, &options); // changes occur immmediately
//unsigned char transmit[20] = "Hello Raspberry Pi!"; // send string
//if ((count = write(file, &transmit, 20))<0){ // transmit
//perror("Failed to write to the output\n");
//return -1;
//}

## Slide 19: Code for Pulse Oximeter
sleep(29); // give the Arduino a chance to respond
unsigned char receive[100]; // declare a buffer for receiving data
printf("<div><h3>Give 30s to respond:/ Thank you for your paitence</div></h3>\n");
if ((count = read(file, (void*)receive, 100))<0){ //receive data
perror("Failed to read from the input\n");
pthread_exit(NULL);
}

## Slide 20: Code for Pulse Oximeter
else if (count==0) printf("There was no data available to read!\n");
else printf("<div><h3>The following was read in [%d]: %s</div></h3></para></html>\n",count,receive);
close(file);
//unsigned char hr = receive[2-4];
//printf("<div><h3>Heartrate : %s</div></h3>\n",hr[2-4]);
//printf("%s",hr);
digitalWrite( 29, LOW );
pthread_exit(NULL);
}

## Slide 21: Code for Pulse Oximeter
int main(int argc, char **argv) {
int policy = SCHED_FIFO;
pthread_t tid;
pthread_attr_t tattr;
int ret;
int newprio = 1;
struct sched_param param;
ret = pthread_attr_init (&tattr);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 1 failed \n ");
return 1;}

## Slide 22: Code for Pulse Oximeter
ret = pthread_attr_getschedparam (&tattr, &param);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 3 failed \n");
return 1;}
param.sched_priority = newprio;
ret = pthread_attr_setschedpolicy(&tattr, policy);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 5 failed \n");
return 1;}

## Slide 23: Code for Pulse Oximeter
ret = pthread_attr_setschedparam (&tattr, &param);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 7 failed \n");
}
int i, rc;
/* create a thread_data_t argument array */
while (1) {
/* create threads */
if ((ret = pthread_create(&tid, &tattr, thr_func, NULL))) {
fprintf(stderr, "error: pthread_create, ret: %d\n", ret);
return EXIT_FAILURE;
}

## Slide 24: Code for Pulse Oximeter
printf("-------------------------------The End---------------------------\n");
pthread_join(tid, NULL);
}
return EXIT_SUCCESS;
}

## Slide 25: Code for DHT and PIR
#include <stdio.h>
#include <stdlib.h>
#include <pthread.h>
#include <wiringPi.h>
#include <stdint.h>
#define MAXTIMINGS 85
#define DHTPIN 7
#define PIRPin 25
int dht11_dat[5] = { 0, 0, 0, 0, 0 };

## Slide 26: Code for DHT and PIR
/* create thread argument struct for thr_func() */
typedef struct _thread_data_t {
int tid;
double stuff;
} thread_data_t;
/* thread function */
void *dht11(void *arg) {
uint8_t laststate = HIGH;
uint8_t counter = 0;
uint8_t j = 0, i;
float f;

## Slide 27: Code for DHT and PIR
dht11_dat[0] = dht11_dat[1] = dht11_dat[2] = dht11_dat[3] = dht11_dat[4] = 0;
wiringPiSetup () ;
pinMode( DHTPIN, OUTPUT );
digitalWrite( DHTPIN, LOW );
delay( 18 );
digitalWrite( DHTPIN, HIGH );
delayMicroseconds( 40 );
pinMode( DHTPIN, INPUT );
for ( i = 0; i < MAXTIMINGS; i++ )

## Slide 28: Code for DHT and PIR
{
counter = 0;
while ( digitalRead( DHTPIN ) == laststate )
{
counter++;
delayMicroseconds( 1 );
if ( counter == 255 )
{
break;
}
}

## Slide 29: Code for DHT and PIR
laststate = digitalRead( DHTPIN );
if ( counter == 255 )
break;
if ( (i >= 4) && (i % 2 == 0) )
{
dht11_dat[j / 8] <<= 1;
if ( counter > 50 )
dht11_dat[j / 8] |= 1;
j++;
}
}

## Slide 30: Code for DHT and PIR
if ( (j >= 40) &&
(dht11_dat[4] == ( (dht11_dat[0] + dht11_dat[1] + dht11_dat[2] + dht11_dat[3]) & 0xFF) ) )
{
f = dht11_dat[2] * 9. / 5. + 32;
printf( "<div><h3>Humidity = %d.%d %% Temperature = %d.%d C (%.1f F)</h3></div>\n",
dht11_dat[0], dht11_dat[1], dht11_dat[2], dht11_dat[3], f );
}else {
printf( "Data not good, skip\n" );
delay(10);
}

## Slide 31: Code for DHT and PIR
pthread_exit(NULL);
}
void *pir(void *arg) {
wiringPiSetup () ;
int t=1;
//char command[] = "clear";
if(wiringPiSetup() == -1){
printf("setup wiringPi failed !");
exit(1);
}
pinMode(PIRPin,INPUT);
if(!(digitalRead(PIRPin))){
printf("<div><h3>Motion not detected</div></h3>\n");
}

## Slide 32: Code for DHT and PIR
else{
printf("<div><h3>Someone is around baby</div></h3>\n");
}
pthread_exit(NULL);
}
int main(int argc, char **argv) {
int policy = SCHED_FIFO;

## Slide 33: Code for DHT and PIR
pthread_t tid,tid1;
pthread_attr_t tattr,tattr1;
int ret,ret1;
int newprio = 1;
int newprio1 = 15;
struct sched_param param,param1;

## Slide 34: Code for DHT and PIR
ret = pthread_attr_init (&tattr);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 1 failed \n ");
return 1;}
ret1 = pthread_attr_init (&tattr1);
if(ret1 != 0) {
printf("pthread_attr_setinheritsched() 2 failed \n");
return 1;}

## Slide 35: Code for DHT and PIR
ret = pthread_attr_getschedparam (&tattr, &param);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 3 failed \n");
return 1;}
ret1 = pthread_attr_getschedparam (&tattr1, &param1);
if(ret1 != 0) {
printf("pthread_attr_setinheritsched() 4 failed \n");
return 1;}

## Slide 36: Code for DHT and PIR
param.sched_priority = newprio;
param1.sched_priority = newprio1;
ret = pthread_attr_setschedpolicy(&tattr, policy);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 5 failed \n");
return 1;}
ret = pthread_attr_setschedpolicy(&tattr1, policy);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 6 failed \n");
return 1;}

## Slide 37: Code for DHT and PIR
ret = pthread_attr_setschedparam (&tattr, &param);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 7 failed \n");
return 1;}
ret1 = pthread_attr_setschedparam (&tattr1, &param1);
if(ret1 != 0) {
printf("pthread_attr_setinheritsched() 8 failed \n");
return 1;}

## Slide 38: Code for DHT and PIR
int i, rc;
/* create a thread_data_t argument array */
while (1) {
/* create threads */
if ((ret = pthread_create(&tid, &tattr, dht11, NULL))) {
fprintf(stderr, "error: pthread_create, ret: %d\n", ret);
return EXIT_FAILURE;
}

## Slide 39: Code for DHT and PIR
printf("priority=%d",param1.sched_priority);
if ((ret1 = pthread_create(&tid1, &tattr1, pir, NULL))) {
fprintf(stderr, "error: pthread_create, ret: %d\n", ret);
return EXIT_FAILURE;
}
pthread_join(tid, NULL);
pthread_join(tid1, NULL);
printf("-------------------------------The End---------------------------\n");
}
return EXIT_SUCCESS;
}

## Slide 40: Code
#include <stdio.h>
#include <stdlib.h>
#include <pthread.h>
#include<fcntl.h>
#include<unistd.h>
#include<termios.h> // using the termios.h library
#include <wiringPi.h>
#define NUM_THREADS 2

## Slide 41: Code
/* create thread argument struct for thr_func() */
typedef struct _thread_data_t {
int tid;
double stuff;
} thread_data_t;
/* thread function */
void *thr_func(void *arg) {

## Slide 42: Code
int t;
printf ("Raspberry Pi wiringPi test program\n");
wiringPiSetupGpio();
pinMode (18, PWM_OUTPUT) ;
pwmSetMode (PWM_MODE_MS);
pwmSetRange (2000);
pwmSetClock (192);
for(t=0;t<=5;t++){

## Slide 43: Code
pwmWrite(18,1);
usleep(100000);
pwmWrite(18,210);
usleep(100000);
}
pwmWrite(18,0);
pthread_exit(NULL);
}

## Slide 44: Code
int main(int argc, char **argv) {
int policy = SCHED_FIFO;
pthread_t tid;
pthread_attr_t tattr;
int ret;
int newprio = 1;
struct sched_param param;

## Slide 45: Code
ret = pthread_attr_init (&tattr);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 1 failed \n ");
return 1;}
ret = pthread_attr_getschedparam (&tattr, &param);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 3 failed \n");
return 1;}

## Slide 46: Code
param.sched_priority = newprio;
ret = pthread_attr_setschedpolicy(&tattr, policy);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 5 failed \n");
return 1;}
ret = pthread_attr_setschedparam (&tattr, &param);
if(ret != 0) {
printf("pthread_attr_setinheritsched() 7 failed \n");
}

## Slide 47: Code
int i, rc;
/* create a thread_data_t argument array */
/* create threads */
if ((ret = pthread_create(&tid, &tattr, thr_func, NULL))) {
fprintf(stderr, "error: pthread_create, ret: %d\n", ret);
return EXIT_FAILURE;
}

## Slide 48: Code
printf("-------------------------------The End---------------------------\n");
pthread_join(tid, NULL);
return EXIT_SUCCESS;
}

## Slide 49: References
MAn7. (2021, June 20). MAN7.org. https://man7.org/linux/man-pages/man3/pthread_setschedparam.3.html. Retrieved Augest 10, 2021, from https://man7.org/linux/man-pages/man3/pthread_setschedparam.3.html
UKdiss. (2021, July 30). Ukdiss. https://ukdiss.com/examples/real-time-operating-systems-advantages-disadvantages.php. Retrieved Augest 10, 2021, from https://ukdiss.com/examples/real-time-operating-systems-advantages-disadvantages.php
Wikipedia. (2021, July 19). Wikipedia. https://en.wikipedia.org/wiki/Real-time_operating_system. Retrieved Augest 10, 2021, from https://en.wikipedia.org/wiki/Real-time_operating_system
Oracle. (2020, 10 15). Oracle homepage. Oracle. https://docs.oracle.com/cd/E19455-01/806-5257/attrib-11564/index.html
QNX. (2020, 12 18). QNX. QNX. http://www.qnx.com/developers/docs/6.3.2/neutrino/lib_ref/p/pthread_attr_getschedparam.html

## Slide 50
THANK YOU