## Slide 1: ESE 4009 IoT based Cradle system using SIDS monitor
Testing components
INSTRUCTOR: Prof. Mike Aleshams
Group 6

## Slide 2: Components used in our project:-
Microprocessor - RASPBERRY PI 3 MOD B+ BCM2837B0
PIR sensor - HC-SR501
USB camera and microphone
Speaker - USB mini speaker
Humidity sensor - DHT11
Electric motor - Servo Motor
Motor Driver - L298N
Pulse Oximeter - MAX30102
GSM/GPRS Module - SIM868

## Slide 3: Microprocessor - RASPBERRY PI 3 MOD B+ BCM2837B0 specifications :
SOC: Broadcom BCM2837B0, Cortex-A53 (ARMv8) 64-bit SoC
CPU: 1.4GHz 64-bit quad-core ARM Cortex-A53 CPU
RAM: 1GB LPDDR2 SDRAM
WIFI: Dual-band 802.11ac wireless LAN (2.4GHz and 5GHz ) and Bluetooth 4.2
Ethernet: Gigabit Ethernet over USB 2.0 (max 300 Mbps). Power-over-Ethernet support (with separate PoE HAT). Improved PXE network and USB mass-storage booting.
Thermal management: Yes
Video: Yes – VideoCore IV 3D. Full-size HDMI
Audio: Yes
USB 2.0: 4 ports
GPIO: 40-pin
Power: 5V/2.5A DC power input
Operating system support: Linux and Unix

## Slide 4: Microprocessor - RASPBERRY PI 3 MOD B+ BCM2837B0 Testing:
1. Add your Raspberry Pi as a host
Start PuTTY. You will see the configuration screen below:
Type the IP address of the Pi into the Host Name
field and click the Open button. If nothing happens when you click the Open button, and you eventually see a message saying Network error: Connection timed out, it is likely that you have entered the wrong IP address for the Pi.
If you do not know the IP address, type hostname -I in the Raspberry Pi command line.

## Slide 5: Microprocessor - RASPBERRY PI 3 MOD B+ BCM2837B0 Testing:
When the connection works you will see the security warning shown below. You can safely ignore it, click the 'Yes' button. You will only see this warning the first time PuTTY connects to a Raspberry Pi that it has not seen before.
You will now see the usual login prompt. Log in with the same username and password you would use on the Pi itself. The default login for Raspberry Pi OS is pi with the password raspberry.

## Slide 6: PIR sensor - HC-SR501 specification
Voltage | 4.8 V – 20 V
Current (idle) | <50 µA
Logic output | 3.3 V / 0 V
Delay time | 0.3 s – 200 s, custom up to 10 min
Lock time | 2.5 s (default)
Trigger | repeat : L = disable , H = enable
Sensing range | <120 °, within 7 m
Temperature | – 15 ~ +70 °C
Dimension | 32 x 24 mm screw-screw 28 mm, M2 Lens diameter: 23 mm

## Slide 7: PIR sensor - HC-SR501 specification

## Slide 8: PIR sensor - HC-SR501 Testing
To test the PIR sensor, we will need following components:
Arduino UNO
PIR Motion Sensor
LED
Jumper Wire

## Slide 9: PIR sensor - HC-SR501 Testing
Follow the steps gives below:-
Connect Vcc pin of PIR sensor to 5v of the arduino
Connect ground pin of PIR sensor to ground pin of the arduino
Coonect output pin of PIR sensor to digital pin 3 of the arduino
Connect LED to arduino (+ve pin to pin 13 and –ve pin to ground
Connect arduino to the computer and upload the code given below:
Copy the code from this website.
https://circuitmagic.com/arduino/pir-motion-sensor-with-arduino/

## Slide 10: PIR sensor - HC-SR501code
int calibrationTime = 30;
int lowIn;
long unsigned int pause = 5000; boolean lockLow = true; boolean takeLowTime; int pirPin = 3; int ledPin = 13;
void setup(){ Serial.begin(9600);
pinMode(pirPin, INPUT);
pinMode(ledPin, OUTPUT);
digitalWrite(pirPin, LOW);
print("calibrating sensor ");
for(int i = 0; i < calibrationTime; i++)
{ Serial.print("."); delay(1000); }
Serial.println(" done");
Serial.println("SENSOR ACTIVE");
delay(50); }
Lvoid loop(){ if(digitalRead(pirPin) == HIGH){ digitalWrite(ledPin, HIGH);
if(lockLow){ //makes sure we wait for a transition to LOW before any further output is made: lockLow = false; Serial.println("---"); Serial.print("motion detected at "); Serial.print(millis()/1000); Serial.println(" sec"); delay(50); } takeLowTime = true; } if(digitalRead(pirPin) == LOW){ digitalWrite(ledPin, LOW); //the led visualizes the sensors output pin state if(takeLowTime){ lowIn = millis(); //save the time of the transition from high to LOW takeLowTime = false; //make sure this is only done at the start of a LOW phase } //if the sensor is low for more than the given pause, //we assume that no more motion is going to happen if(!lockLow && millis() - lowIn > pause){ //makes sure this block of code is only executed again after //a new motion sequence has been detected lockLow = true;
Serial.print("motion ended at ");
Serial.print((millis() - pause)/1000);
Serial.println(" sec");
delay(50); } } }

## Slide 11: PIR sensor - HC-SR501 Testing
Open Arduino software and go to file menu and open program file
Add code and go to tool menu and make sure port arduino COM is selected
Upload the program and open serial monitor
We will see the LED turn on whenever motion is detected

## Slide 12: Speaker - USB mini speaker from Adafruit specification
Voltage: 5V
Total power: 2 x 2W
SNR: 60dB
Impedance: 4 ohm
Cable Length: 1,168mm / 46"
Product Weight: 73.6g / 2.6oz

## Slide 13: Speaker - USB mini speaker from Adafruit : testing
It is very easy to test this component.
We can directly connect the speaker with the computer using the USB cable and play some music to test it.

## Slide 14: Humidity sensor : DTH11 Specifications :
Accuracy:±5%
Humidity Range:20 ~ 80% RH
Mounting Type: Through Hole
Operating Temperature:0°C ~ 50°C
Output:16b
Output Type: Digital
Package / Case: Housed Sensor
Response Time:1s
Sensor Type: Humidity, Temperature
Voltage - Supply:3V ~ 5V

## Slide 15: Humidity sensor : DTH11 Testing :
Connect the DTH11 sensor with arduino as shown below :
Click to add text
R1: 10K Ohm pull up resistor

## Slide 16: Humidity sensor : DTH11 Testing :
Install the DHTLib library. Download the DHTLib.zip file below and open up the Arduino IDE. Then go to Sketch>Include Library>Add .ZIP Library and select the DHTLib.zip file
https://www.circuitbasics.com/wp-content/uploads/2015/10/DHTLib.zip
After it’s installed, upload this example program to the Arduino and open the serial monitor:
You should see the humidity and temperature readings displayed at one second intervals.

## Slide 17
Humidity sensor : DTH11 Testing :​ code
​
​
#include <dht.h>
#define PIN7// sensor is connected to pin 7 of Arduino
dht DHT;
void setup(){ //start setup
Serial.begin(9600);
delay(500); //Delay to let system boot
Serial.println("DHT11 Humidity & temperature Sensor\n\n");
delay(1000); //Wait before accessing Sensor
} //end "setup()"
void loop(){ //Start of Program
DHT.read11(dht_apin);
Serial.print("Current humidity = ");
Serial.print(DHT.humidity); //print humidity in percentage
Serial.print("% ");
Serial.print("temperature = ");
Serial.print(DHT.temperature); //print temperature in C
Serial.println("C ");
delay(5000); //Wait 5 seconds before accessing sensor again.
} // end loop

## Slide 18: GSM/GPRS Module – SIM868 specifications :
Raspberry Pi connectivity, compatible with Raspberry Pi 2B/3B/Zero/Zero W
Supports SMS, phone call, GPRS, DTMF, HTTP, FTP, MMS, email, etc.
Bluetooth 3.0, supports data transferring through Bluetooth
Onboard USB TO UART converter CP2102 for UART debugging
Frequency Bands: 850/900/1800/1900MHz
Other specification

## Slide 19: GSM/GPRS Module – SIM868 Testing:
Insert the GSM (not CDMA) SIM card to GSM module and lock it.
Connect the adapter to GSM module and turn it ON!
The red LED with turn on as soon as you connect to power. This confirms that the board is receiving power.
The other LED with blink. First it will blink faster as it is searching for network.
Now wait for some time (say 1 minute) and see the blinking rate of ‘status LED’ or ‘network LED’

## Slide 20: GSM/GPRS Module – SIM868 Testing:
Once the connection is established successfully, the status/network LED will blink continuously every 3 seconds.
You may try making a call to the mobile number of the sim card inside GSM module. If you hear a ring back, the gsm module has successfully established network connection.
Also, when we make a call, the other LED named "ring" should turn on. This will make sure that the GSM board is working fine.

## Slide 21: Pulse Oximeter – MAX30102 specifications:
Heart-Rate Monitor and Pulse Oximeter Biosensor in LED Reflective Solution
Tiny 5.6mm x 3.3mm x 1.55mm 14-Pin Optical Module
  Integrated Cover Glass for Optimal, Robust Performance
Ultra-Low Power Operation for Mobile Devices
  Programmable Sample Rate and LED Current for Power Savings
  Low-Power Heart-Rate Monitor (< 1mW)
  Ultra-Low Shutdown Current (0.7µA, typ)

## Slide 22: Pulse Oximeter – MAX30102 Specifications :
Fast Data Output Capability
  High Sample Rates
Robust Motion Artifact Resilience
  High SNR
-40°C to +85°C Operating Temperature Range

## Slide 23: Pulse Oximeter – MAX30102 Testing :
We use only 3.3V and GND pin.
The protocol that attributes is the I2C (SCA,SCL)

## Slide 24: Pulse Oximeter – MAX30102 Testing :
Code: https://create.arduino.cc/projecthub/code_files/440367/download

## Slide 25: Pulse Oximeter – MAX30102 Testing : code
#include <Wire.h>
#include "MAX30100_PulseOximeter.h"
#define REPORTING_PERIOD_MS 1000
PulseOximeter pox;
uint32_t tsLastReport = 0;
void onBeatDetected()
{
Serial.println("Beat!");
}
void setup()
{
Serial.begin(115200);
Serial.print("Initializing pulse oximeter..");
if (!pox.begin()) {
Serial.println("FAILED");
for(;;);
} else {
Serial.println("SUCCESS");
}
pox.setIRLedCurrent(MAX30100_LED_CURR_7_6MA);
​
// Register a callback for the beat detection​
pox.setOnBeatDetectedCallback(onBeatDetected);​
}​
​void loop()​
{​
pox.update();​
if (millis() - tsLastReport > REPORTING_PERIOD_MS) {​
Serial.print("Heart rate:");​
Serial.print(pox.getHeartRate());​
Serial.print("bpm / SpO2:");​
Serial.print(pox.getSpO2());​
Serial.println("%");​
​
tsLastReport = millis();​
}​
}

## Slide 26: Pulse Oximeter – MAX30102 Testing :
Connection:
Connect Vcc of pulse oximeter with 3.3V of Arduino
Connect ground pin of pulse oximeter with ground pin of Arduino
Connect SCL of pulse oximeter with SCL of Arduino
Connect SDA of pulse oximeter with SDA of Arduino

## Slide 27: USB Camera
Full HD Webcam 1080P , Full HD Webcam 1080P provides more clarity video calling, streaming, conferencing, Max Resolution up to 1920 x 1080 pixels never miss any details.
110 Degree Wide-Angle Webcam with Stereo Microphone , Fixed focus desktop and laptop Webcam captures FULL HD video at a wide angle of up to 110 degrees. Great for webinars, video conferencing, live streaming, etc.
PLUG AND PLAY Easy to use.

## Slide 28: Servo Motor testing
You can connect small servo motors directly to an Arduino to control the shaft position very precisely. But we will connect servo motor using L298N to ensure it will not stop due to power shortage.
Because servo motors use feedback to determine the position of the shaft, you can control that position very precisely. As a result, servo motors are used to control the position of objects, rotate objects, move legs, arms or hands of robots, move sensors etc. with high precision. Servo motors are small in sizes, and because they have built-in circuitry to control their movement, they can be connected directly to an Arduino.

## Slide 29: Servo Motor testing
Most servo motors have the following three connections:
Black/Brown ground wire.
Red power wire (around 5V).
Yellow or White PWM wire.
In this experiment, we will connect the power and ground pins directly to the Arduino 5V and GND pins. The PWM input will be connected to one of the Arduino's digital output pins.

## Slide 30: Wirring
Servo red wire – 5V pin Arduino
Servo brown wire – Ground pin Arduino
Servo yellow wire – PWM(9) pin Arduino
code: https://www.allaboutcircuits.com/projects/servo-motor-control-with-an-arduino/#loginModal

## Slide 31: Servo Motor testing: code
#include //Servo library Servo servo_test; //initialize a servo object for the connected servo
int angle = 0; void setup() { servo_test.attach(9); // attach the signal pin of servo to pin9 of arduino } void loop() { for(angle = 0; angle < 180; angle += 1) // command to move from 0 degrees to 180 degrees { servo_test.write(angle); //command to rotate the servo to the specified angle delay(15); } delay(1000); for(angle = 180; angle>=1; angle-=5) // command to move from 180 degrees to 0 degrees { servo_test.write(angle); //command to rotate the servo to the specified angle delay(5); } delay(1000); }

## Slide 32: Motor Driver L298N Testing
1.) The controller can take up to 2 DC motors. Plug one DC motor into the terminal labelled OUT1 and OUT2. Plug the second DC motor into the terminal labelled OUT3 and OUT4:

## Slide 33: Motor Driver L298N Testing
We will test our motor driver with the continuity test. We can also test it using Arduino, but for that we would need a DC motor. So here we will be using multimeter to check the connectivity. We will first check the connection between IN1 and OUT1 and then we will check the connection between IN2 and OUT2. There should be beep sound on multimeter is the connection is proper. By this test, we can see that the motor driver is not damaged and the connection are proper.

## Slide 34: References
Vivek Gite, March 14, 2018,Raspberry PI 3 model B+ Released: Complete specs and pricing,https://www.cyberciti.biz/hardware/raspberry-pi-3-model-b-released-specs-pricing/
Batz, V. M. (2019, January 4). Introducing PiCockpit and PiDoctor – how to test your Raspberry Pi and get information about it. Pi3g.com. https://pi3g.com/2019/01/05/introducing-picockpit-and-pidoctor-how-to-test-your-raspberry-pi-and-get-information-about-it.
HC-SR501 PIR Motion Sensor Module. Elektor. (n.d.). https://www.elektor.com/hc-sr501-pir-motion-sensor-module.
Industries, A. (n.d.). Mini External USB Stereo Speaker. adafruit industries blog RSS. https://www.adafruit.com/product/3369
Scott Campbell,HOW TO SET UP THE DHT11 HUMIDITY SENSOR ON AN ARDUINO, https://www.circuitbasics.com/how-to-set-up-the-dht11-humidity-sensor-on-an-/arduino/

## Slide 35: Reference
Datasheet of MAX30102, https://datasheets.maximintegrated.com/en/ds/MAX30100.pdf
Ryan Chan,July 17, 2020,How to use the L298N Motor Driver, https://create.arduino.cc/projecthub/ryanchan/how-to-use-the-l298n-motor-driver-b124c5
Iasonas Christoulakis, January 6, 2021, Measure SpO2, Heart Rate and BPT Using Arduino, https://create.arduino.cc/projecthub/iasonas-christoulakis/measure-spo2-heart-rate-and-bpt-using-arduino-68724d?ref=part&ref_id=10308&offset=9
HD Webcam 1080P with Microphone, PC Laptop Desktop USB Webcams, Pro Streaming Computer Camera, 110-Degree Widescreen. Amazon.ca: Electronics. (n.d.). https://www.amazon.ca/Microphone-Streaming-Conferencing-110-Degree-Widescreen/dp/B081Z2NX9W.

## Slide 36: Thank You